Personal Tracker

User Manual

- Starting Up

Press power button after LED 3 flashes, device boot

- Power off

Press power button till one time LED flash, Device Power off

- SMS Positioning

Edit SMS “6660000” to cell phone number in the device, it returns current position and a map link as well

- Dialing Positioning

Dial the cell phone number in the device get through and hang up, automatically returns current position and a map link as well.

- Set & Clear E-fence

Login platform press and fence settings

- Track Playback

Login platform http://m.gps588.com, input IMEI last 8 digits, you can check the track display.

- SOS Call settings

Send SMS (#711#Called mobile phone number#serial number#0000#1##, settings success returns CONFIG OK or returns PASSWORD ER if your settings failed on contrary.

Note: This device can combine 9 called mobile phone number, serial number is (1---9)

- Voice Call

  - Dial through the mobile phone number in the device 1-5 seconds access talking mode, plug in earphone can communicate with each other.

  - Press SOS, it will dial combined mobile phone number(1---9)

- Power Saving Mode Settings

Send commands brackets below to the mobile phone number in the device, reply “CONFIT OK”, setting success.

Super power saving mode (#730#37#1#0000##) Standby 8 days

Middle power saving mode (#730#32#1#0000##) Standby 5 days

General power saving mode (#730#30#1#0000##) Standby 3 days

- Modify Password

Send SMS “#command code(770)#new password(4digit)# password(4digit)##. Settings success returns CONFIG OK or returns PASSWORD ER if your settings failed on contrary.

e.g.: #770#1111#0000##, after execution of the command, password turns to 1111 from 0000

Note: Device initial password is 0000

- Product Specification

Dimensions: L: 44mm     W: 37mm   H: 12mm

Weight: 45g